## Slide 1: 5-3 Serial Peripheral Interface SPI
Doing serial Fast

## Slide 2: Day 5-3
Assignment:
HW 06, Due Tuesday
Today’s Topics:
Projects
SPI
LCD

## Slide 3: SPI: Intro
Serial Peripheral Interface (SPI) is an interface bus commonly used to send data between microcontrollers and small peripherals
  (shift registers, sensors, and SD cards)
It uses separate clock and data lines, along with a select line to choose the device you wish to talk to.
From: https://learn.sparkfun.com/tutorials/serial-peripheral-interface-spi

## Slide 4: I2C - FlashBack
“two-wire interface” standard
Used to attach low-speed peripherals to embedded systems

## Slide 5: SPI: Intro
Serial Peripheral Interface (SPI) is an interface bus commonly used to send data between microcontrollers and small peripherals
  (shift registers, sensors, and SD cards)
It uses separate clock and data lines, along with a select line to choose the device you wish to talk to.
From: https://learn.sparkfun.com/tutorials/serial-peripheral-interface-spi

## Slide 6: SPI - Clock
One side generates the clock
Called the master (only one)
Other side is called the slave
There are two data lines
  MOSI – Master Out / Slave In
  MISO – Master In / Slave Out

## Slide 7: Slave Select
Tells slave it should wake up.
Used if multiple slaves
SS or CS (chip celect)

## Slide 8: Multiple Slaves
Use multiple Chip Selects
  SP1.1 and SP1.2 on Blue
Daisy-chain
  Used with addressable LEDs

## Slide 9: LCD Display
MISO
LED
SCK
MOSI
DC
Reset
CS
GND
VCC

## Slide 10: Wiring LCD

## Slide 11: LCD Software
bone$ cd exercises/displays/ili9341
bone$ ./on.sh
bone$ ./off.sh
bone$ ./reset.sh

## Slide 12: On.sh
sudo bash << EOF
UNEXPORT= /sys/class/gpio/unexport
echo 113 > $UNEXPORT # RESET - GP0_6
echo 116 > $UNEXPORT # D/C - GP0_5
OCP=/sys/devices/platform/ocp
echo gpio > $OCP/ocp:P9_28_pinmux/state # RESET- P9_28 - GP0_6
echo gpio > $OCP/ocp:D13_pinmux/state # D/C - D13 - GP0_5

## Slide 13: On.sh - 2
sudo bash << EOF
…
echo spi > $OCP/ocp:P9_31_pinmux/state # SCLK - S1.1_5
echo spi > $OCP/ocp:P9_29_pinmux/state # MISO - S1.1_4
echo spi > $OCP/ocp:P9_30_pinmux/state # MOSI - S1.1_3

## Slide 14: On.sh - 3
sudo bash << EOF
…
echo 29 > $UNEXPORT # CS - H18
echo spi > $OCP/ocp:H18_pinmux/state # CS - S1.1_6

## Slide 15: On.sh - 4
sudo bash << EOF
…
sleep 1
# Insert the framebuffer modules
modprobe fbtft_device name=adafruit28 busnum=1 rotate=90 \
gpios=reset:113,dc:116 cs=0
EOF

## Slide 16: modinfo
bone$ modinfo fbtft_device
filename: /lib/modules/4.4.84-ti-r120/kernel/drivers/staging/fbtft/fbtft_device.ko
license: GPL
author: Noralf Tronnes
description: Add a FBTFT device.
depends: fbtft
staging: Y
intree: Y
vermagic: 4.4.84-ti-r120 SMP mod_unload modversions ARMv7 p2v8

## Slide 17: modinfo
parm: name:Devicename (required). name=list => list all supported devices. (charp)
parm: rotate:Angle to rotate display counter clockwise: 0, 90, 180, 270 (uint)
parm: busnum:SPI bus number (default=0) (uint)
parm: cs:SPI chip select (default=0) (uint)
parm: speed:SPI speed (override device default) (uint)
parm: mode:SPI mode (override device default) (int)
parm: gpios:List of gpios. Comma separated with the form: reset:23,dc:24 (when overriding the default, all gpios must be specified) (charp)
parm: fps:Frames per second (override driver default) (uint)
parm: gamma:String representation of Gamma Curve(s). Driver specific. (charp)

## Slide 18: modinfo
parm: txbuflen:txbuflen (override driver default) (int)
parm: bgr:BGR bit (supported by some drivers). (int)
parm: startbyte:Sets the Start byte used by some SPI displays. (uint)
parm: custom:Add a custom display device. Use speed= argument to make it a SPI device, else platform_device (bool)
parm: width:Display width, used with the custom argument (uint)
parm: height:Display height, used with the custom argument (uint)
parm: buswidth:Display bus width, used with the custom argument (uint)
parm: init:Init sequence, used with the custom argument (array of int)
parm: debug:level: 0-7 (the remaining 29 bits is for advanced usage) (ulong)
parm: verbose:0 silent, >0 show gpios, >1 show devices, >2 show devices before (default=3) (uint)

## Slide 19: On.sh - 4
sudo bash << EOF
…
sleep 1
# Insert the framebuffer modules
modprobe fbtft_device name=adafruit28 busnum=1 rotate=90 \
gpios=reset:113,dc:116 cs=0
EOF

## Slide 20: FrameBuffers
Once the modprobe is run
/dev/fb0 appears
You can read and write to it.
bone$ cat /dev/fb0 > /tmp/backup
bone$ cat /tmp/backup > /dev/fb0

## Slide 21: Programs use it
Display an image
bone$ fbi -noverbose -T 1 -a boris.png
Play a movie
bone$ mplayer RedsNightmare.mpg
pygame

## Slide 22: mmap
You can open it with mmap

## Slide 23: Framebuffer.c
// Open the file for reading and writing
fbfd = open("/dev/fb0", O_RDWR);
if (fbfd == -1) {
perror("Error: cannot open framebuffer device");
// Open the file for reading and writing fbfd = open("/dev/fb0", O_RDWR); if (fbfd == -1) { perror("Error: cannot open framebuffer device"); exit(1); } printf("The framebuffer device was opened successfully.\n"); exit(1);
}
printf("The framebuffer device was opened successfully.\n");

## Slide 24: Framebuffer.c - 2
// Figure out the size of the screen in bytes
screensize = vinfo.xres * vinfo.yres * vinfo.bits_per_pixel / 8;
// Map the device to memory
fbp = (char *) mmap(0, screensize, PROT_READ | PROT_WRITE, MAP_SHARED, fbfd, 0);
if ((int)fbp == -1) {
perror("Error: failed to map framebuffer device to memory");
exit(4);
}
printf("The framebuffer device was mapped to memory successfully.\n");

## Slide 25: Framebuffer.c - 3
// Figure out where in memory to put the pixel
location = (x+vinfo.xoffset) * (vinfo.bits_per_pixel/8) +
(y+vinfo.yoffset) * finfo.line_length;
int r = 0; // 5 bits
int g = 0; // 6 bits
int b = 31; // 5 bits
unsigned short int t = r<<11 | g << 5 | b;
*((unsigned short int*)(fbp + location)) = t;

## Slide 26: Screen Size
// Get fixed screen information
if (ioctl(fbfd, FBIOGET_FSCREENINFO, &finfo) == -1) {
perror("Error reading fixed information");
exit(2);
}
// Get variable screen information
if (ioctl(fbfd, FBIOGET_VSCREENINFO, &vinfo) == -1) {
perror("Error reading variable information");
exit(3);
}

## Slide 27: Reset.sh
sudo bash << EOF
# Save contents of framebuffer
cat /dev/fb0 > /tmp/fb0
# Disable the framebuffer
rmmod fbtft_device
sleep 1

## Slide 28: Reset.sh
sudo bash << EOF
# Get access to the RESET pin
echo 49 > /sys/class/gpio/export # RESET - V14 - GP0_PIN4
sleep 1
# Toggle it
echo out > /sys/class/gpio/gpio49/direction
echo 0 > /sys/class/gpio/gpio49/value
echo 1 > /sys/class/gpio/gpio49/value
# Remove access so the framebuffer can use it
echo 49 > /sys/class/gpio/unexport # RESET - GP0_PIN4

## Slide 29: Reset.sh
# Fire up the framebuffer
echo Firing up framebuffer
sleep 1
modprobe fbtft_device name=adafruit28 busnum=1
rotate=270 gpios=reset:113,dc:116 cs=0
# Restore the image
cat /tmp/fb0 > /dev/fb0
EOF